## Slide 1: MoNDE: Mixture of Near-Data Experts for Large-Scale Sparse Models
Taehyun Kim1,2, Kwanseok Choi1, Youngmock Cho1,2,
Jaehoon Cho1, Hyuk-Jae Lee1,2, Jaewoong Sim1
1Seoul National University 2Inter-University Semiconductor Research Center
Notes: Hello, my name is Taehyun Kim.
I’d like to present our work, “MoNDE, Mixture of Near-Data Experts for Large-Scale Sparse Models”.
This work was conducted by my colleagues, supervisors and myself at Seoul National University.

## Slide 2: Large Language Models in our Daily Lives
Question Answering
Code Generation
Machine Translation
Notes: Over the recent years, Transformer-based large language models, or LLMs, have revolutionized the use of AI in our daily lives.
Today, we can easily access LLM services for tasks such as question answering, machine translation, and software code generation.

## Slide 3: Large Language Models in our Daily Lives
Moore’s Law for NLPs : “Model sizes increase exponentially every year”
Chart: Year
| 2018.1 | 2018.9 | 2019.1 | 2019.9 | 2020.4 | 2021.8 | 2022.1 | 2022.1 | 2022.1 | 2022.5 | 2022.5 | 2023.25 | 2023.9166666666667 | 2024.25
Models | 110 | 340 | 1500 | 11000 | 175000 | 530000 | 26000 | 395000 | 1571000 | 54000 | 1200000 | 1760000 | 90000 | 317000
GPU | 8000 | 8000 | 12000 | 20000 | 12000 | 20000 | 12000 | 35250
label | 100 | 1000 | 10000 | 100000 | 1000000
Budget
Shortage
Notes: This outstanding model performance can largely be attributed to unprecedented model sizes, which are expected to grow exponentially every year. //
However, scaling model capacity inevitably leads to an increase in computational costs and memory requirements, // making it increasingly difficult to train and serve due to limited hardware budgets.

## Slide 4: Mixture-of-Experts (MoE)
Scale model capacity without proportionally increasing computation
Fixed-complexity computation
Large memory
complexity
Attention
Transformer Block
Linear1
Activation
Linear2
Dense FFN
× B
Expert
FFN1
Expert
FFN2
Expert
FFN3
MoE FFN
Dense↔MoE
Conversion
Input Tokens
1
2
3
token1
token1
1
token1
token1
token2
token2
2
token1
token2
token1
token2
3
token3
token3
Top-2
Gating
Gating
Notes: Recently, mixture-of-experts, or in short MoE, has been applied to large language models in order to scale model capacity without proportionally increasing the computation.
//
The original transformer model architecture mainly consists of multiple transformer blocks, which is each made up of an attention module and feedforward network., or in short FFN.
//
In MoE Transformers, the FFN is duplicated into multiple experts, each corresponding to a dense FFN.
// // // //
A gating network is added to map each input token to k experts to process the token.
The computational load is analogous to k dense networks, instead of being proportional to the total number of experts.
//
Although MoE offers the promise of fixed-complexity computation, the large memory complexity remains a challenge.

## Slide 5: Mixture-of-Experts (MoE)
Significant memory demands that scale to expert and embedding sizes
Chart: Number of Experts (NLLB-MoE)
| Dense | E=64 | E=128 | E=256 | E=512
Non-MoE | 13.3731 | 11.3662 | 11.3724 | 11.385 | 11.4102
MoE | 0 | 103.0792 | 206.1584 | 412.3169 | 824.6337
Scales linearly to the
number of experts
4× NVIDIA A100 (320 GB)
1× NVIDIA A100 (80 GB)
Scales quadratically to the embedding size
Chart: Embedding size
| 768 | 1536 | 3072 | 6144 | 12288
Tokens (6144×) | 0.017578 | 0.035156 | 0.070312 | 0.14062 | 0.28125
Single Expert | 0.017578 | 0.070312 | 0.28125 | 1.125 | 4.5
Chart: Embedding size
| 768 | 1536 | 3072 | 6144 | 12288
Tokens (6144×) | 0.017578 | 0.035156 | 0.070312 | 0.14062 | 0.28125
Single Expert | 0.017578 | 0.070312 | 0.28125 | 1.125 | 4.5
Expert/Tokens | 1 | 2 | 4 | 8 | 16
Notes: In particular, MoE large language models have significant memory demands that scale to expert and embedding sizes.
//
Because memory requirement scales linearly to the number of experts, // MoEs that adopt hundreds of experts may easily surpass the memory capacity of a single commodity GPU or even multi-GPU settings.
//
In addition, the memory requirement scales quadratically to embedding sizes.
//
Compared to the data volume of 6144 tokens which scales only linearly, the size of every expert module scales much faster.

## Slide 6: Existing Solution : Expert Parallelism
64 experts / 1 GPU → 16 experts / GPU × 4 GPUs
Expert Parallelism and its Resource-Inefficiency
Token 1
GPU2
GPU3
GPU4
GPU1
Experts
17-32
Experts
32-48
Experts
49-64
Experts
1-16
Gate
Token 1
Token 1
GPU1
Experts
1-64
Gate
Token 1
Notes: To combat large memory requirements of large MoEs, // expert parallelism in multi-GPU settings equally divides experts across GPUs.
When an expert in another GPU is activated, the input and output tokens are transferred back and forth the associated GPUs for processing the activated expert.

## Slide 7: Existing Solution : Expert Parallelism
Valuable GPUs used for storing expert data, not utilizing the compute
Token 1
Expert Parallelism and its Resource-Inefficiency
GPU2
GPU3
GPU4
GPU1
Experts
17-32
Experts
32-48
Experts
49-64
Experts
1-16
Gate
Token 1
Idle
Idle
Idle
Notes: However, expert parallelism could result in high GPU underutilization especially in low-batch inference settings, since GPUs without activated experts are idle during expert processing.
This means that valuable GPUs are used mainly for storing expert data and not utilizing the compute capabilities of the GPUs, which is resource-inefficient.

## Slide 8: Existing Solution : Expert Offloading
Leverage for MoE Inference (ours)
512 GB/s
CXL
NDP
1 TB
Store Experts
2 TB/s
200 GB/s
GPU
HBM
80 GB
DDR
CXL
xDDR
CPU
PCIe
Bus
32 GB/s
32 GB/s
32 GB/s
Fetch experts
for computation
Bottleneck
Notes: Alternatively, another line of work named expert offloading addresses the GPU memory shortage in a more resource-efficient way.
//
This method offloads massive expert parameters to secondary memory spaces such as the CPU memory which is connected to the GPU by the PCIe.
//
The expert parameters are transferred to the GPU on-the-fly when needed for computation.
//
However, the massive expert transfers over low-bandwidth PCIe introduce large latency overheads, making it unsuitable for latency-critical inference tasks.
//
Meanwhile, near-data processing technology is actively being developed for deployment to emerging CXL memory devices.
//
We leverage this opportunity to process MoE operations using near-data processing, which could replace up to dozens of expert-parallel GPUs and also avoid heavy expert transfer overheads.

## Slide 9: Key Insight : Activations are Cheaper to Move
Near-data processing (NDP) for MoE experts → Replace PMove with AMove
Parameter Movement (PMove)
GPU
Memory Device
PCIe (BW↓)
Attention
Gate
Expert FFN
MoE
Attention
Expert FFN
MoE
Activation Movement (AMove) + NDP
Memory Device
GPU
Attention
Gate
Expert FFN
MoE
Attention
Expert FFN
MoE
Activation
PCIe (BW↓)
Activation
Near-Data Processing
Notes: Our key insight is that token activations are smaller and cheaper to move than experts.
//
The existing expert offloading method relies on parameter movement, or PMove, to fetch the necessary experts to the GPU for processing.
//
As mentioned earlier, this method is highly bottlenecked by heavy expert movement.
//
Meanwhile, we propose a near-data processing solution for processing MoE experts in the memory device where they reside.
//
Our idea replaces heavy parameter movement with cheap activation movement.

## Slide 10: MoNDE : Mixture of Near-Data Experts
NDP solution built on top of emerging CXL memory devices
MoNDE Device
GPU
System
Memory
CXL I/F
PCIe Bus (BW↓)
Host CPU
System Overview
CXL Controller .
LPDDR DRAM
Decoder
Mem
Req
Queue
mmap
Regs
Regular
DRAM
Buf
NDP
Req
Queue
Inst
Buf
Mem Ctrl (BW↑)
NDP
Unit
SIMD
Ctrl
Scratch
pad
MAC
Array
Unit
Act
Buf
Exp
Buf
Skew Unit
Vec Unit
u
NDP Controller .
v
NDP Core .
w
Device Memory .
x
MoNDE Device Overview
High density & bandwidth
Specialized expert unit
mmap
Regs
Decoupled Control
Notes: We propose MoNDE, Mixture of Near-Data Experts, a near-data processing solution built on top of emerging CXL memory devices.
//
The MoNDE device is deployed in a typical GPU system as a PCIe add-in card.
//
Each MoNDE device features a device memory, near-data processing core and controllers.
//
The device memory is designed on latest DRAM technologies, which offer high density and bandwidth enabled by recent advancements in die stacking and bonding.
//
The near-data processing core includes matrix units and vector units which are specialized at processing the matrix multiplications and feature activation layers such as ReLU and GeLU, that comprise each MoE expert operation.
//
Furthermore, the MoNDE controllers provide an efficient near-data processing schedule that resembles the widespread CUDA.
By decoupling the control pipeline, the MoNDE device could process expert operations in parallel with the GPU pipeline.

## Slide 11: MoNDE Execution Flow
a
a
GPU
+ MoNDE
g
e
e
e
e
e
GPU
PCIe
MoNDE
GPU
+ Offload
g
p
p
p
p
p
e
e
e
e
e
GPU
PCIe
Mem. Dev.
g
Gating
e
Expert
PMove
p
a
AMove
Time
Ideal GPU
g
e
e
e
e
e
GPU
PCIe
Mem. Dev.
Streams
Notes: We demonstrate the execution flow of MoNDE for which 5 experts are activated.
The ideal GPU with infinite memory assumes that all experts are stored on the GPU, and is capable of running the expert operations continuously.
//
The expert offloading scheme must first fetch the expert parameters from secondary memory before running the expert computations on the GPU.
//
Transferring large amount of data across the PCIe causes a large overhead.
//
In MoNDE, the relatively small token activation data is transferred to the MoNDE device, where the expert operations are executed.
//
The resulting output activations are sent back to the GPU for subsequent network layers.
Because the data transfer is much smaller, MoNDE near-data processing reduces latency, even when the processing time of each expert is longer than that of the GPU.

## Slide 12: GPU-MoNDE Load-balancing
Exploit expert load imbalance
Chart: Routed Tokens (Total avg. 786 tokens)
| 0 | 1-3 | 4-15 | 16-31 | 32-63 | 64-127 | 128+
Average over 5 translation tasks | 34.0717 | 58.7833 | 30.2817 | 0.51167 | 1.3233 | 1.6667 | 1.3717
Top 2% experts process 50% of tokens
→ Run hot experts on the GPU!
Chart: Operational Intensity (Ops/Byte)
| 1.0000000000000002E-2 | 0.1 | 1 | 9.9999999999999982 | 100 | 1000
NVIDIA A100 | 19.49 | 194.9 | 1949 | 19490 | 19490 | 19490
NLLB-MoE Expert | 684.7843 | 1420.2934 | 5534.7517 | 12341.86 | 14364.4391 | 15004.2526 | 15936.7989
ylabel | 100 | 1000 | 10000 | 100000
Hot experts utilize GPU better
Remaining experts run
comparably on MoNDE NDP
How many hot experts should be run
on the GPU?
Notes: To reduce inference latency when there are many tokens to process, we propose GPU-MoNDE load-balancing for running expert operations on the GPU and MoNDE NDP in parallel.
//
In order to effectively load-balance the two processors, we exploit expert load imbalance.
This means that the token distribution to the MoE experts is skewed.
We show a histogram of the number of experts that receives a certain range of token counts represented on the x axis.
We average over 5 translation tasks using the NLLB-MoE model, with 786 input tokens on average per batch.
//
We found that out of 128 experts, the top 2% of experts process over 50% of the input tokens.
//
Due to this imbalance, there exists a significant gap in the compute-to-memory ratio for the computations of the hot experts and the remaining experts.
//
We analyze that the hot expert operations utilize the GPU better, and hence we run the hottest experts on the GPU.
//
The majority of the remaining experts process only a few tokens.
Such expert operations are memory bandwidth-bound, and underutilizes the GPU compute.
This means that a weaker compute unit like the MoNDE NDP could obtain comparable performance by leveraging high memory bandwidth.
//
This leaves the question: how many hot experts should be run on the GPU?

## Slide 13: GPU-MoNDE Load-balancing
Overlap GPU and MoNDE pipelines
MoNDE Device
Expert FFN
MoNDE Memory
Expert FFN
MoNDE NDP
GPU
Expert FFN
GPU Memory
Expert Parameter Movement
NDP Expert Load
Load-balancing Scheduler (Host CPU Runtime)
1
1
2
3
Notes: To answer this question, we implement a load-balancing scheduler that overlaps the GPU and MoNDE pipelines.
Recall that the GPU pipeline consists of expert parameter movement followed by GPU expert processing, whereas the MoNDE pipeline consists of activation movement, near-data expert processing and another activation movement.
//
Our scheduler balances the latencies for expert parameter movement of the GPU pipeline, and the expert parameter load time of the MoNDE pipeline, which are the main sources of latency for the two pipelines.
//
We formulate the two latencies as the expert parameter sizes divided by the bandwidths of the PCIe and MoNDE device memory, which can be obtained through system profiling.
//
The scheduler follows three steps :
//
First, the MoE gating function determines the total number of activated experts, which is the sum of the experts to be processed on the GPU and the MoNDE Near-Data Processor.
//
Next, the latencies of the GPU and MoNDE pipelines are equated.
//
We remove the GPU expert processing time and the activation movement time because they are relatively small.
//
Using the two equations obtained from the previous steps, the scheduler estimates the optimal number of the top hot experts to offload to the GPU.

## Slide 14: GPU-MoNDE Load-balancing
Minimally moves expert parameters & Utilize GPU-NDP parallelism
GPU
PCIM→G
PCIG→M
MoNDE
GPU
+ MoNDE
+ Load-balancing
g
a
a
p
p
e
e
e
e
e
GPU
PCIe
MoNDE
GPU
+ MoNDE
Streams
g
a
a
e
e
e
e
e
Time
g
Gating
e
Expert
PMove
p
a
AMove
Computation Overlap
Notes: GPU-MoNDE load-balancing reduces the total latency by minimally moving expert parameters // and overlapping the computations of the GPU and the MoNDE near-data processor.

## Slide 15: Evaluation Setting
Integrate Pytorch implementation with in-house cycle-accurate simulator
System |  | 
Processor | NVIDIA A100 GPU | MoNDE
Compute (BF16) | 312 TOPS | 2 TOPS
Memory | 80 GB 2 TB/s | 512 GB 512 GB/s
PCIe | PCIe gen4 32 GB/s | 
Workload |  | 
Model | Switch Transformers (Top-1 gating) | NLLB-MoE (Top-2 gating)
Experts per MoE | 128 (each 8.4 MB) | 128 (each 33.6 MB)
Layers (Non-MoE/MoE) | 24 / 24 | 36 / 12
Model Size (Dense/MoE) | 1.1 GB / 51.5 GB | 5.7 GB / 103.1 GB
Task | XSum (Summarization) | FLORES-200 (Machine Translation)
Notes: For our evaluation, we implement the MoNDE pipeline using Pytorch, and integrate it with an in-house cycle-accurate simulator that models the MoNDE Near-data processor.
We do this by first running MoNDE functions with the CPU and replacing the associated latencies with that of the simulated MoNDE near-data processor.
//
Our test system includes an NVIDIA A100 GPU and a simulated MoNDE device with 512 GB capacity and 512 GB/s memory bandwidth.
The processing power of the near-data processor is 2 Tera-operations per second.
//
We test Switch Transformers and NLLB-MoE models on a summarization task and machine translation task, respectively.

## Slide 16: Evaluation
MoNDE achieves 4.9× and 1.5× speedups for the encoder and decoder
Chart: Norm. Throughput
| B=1 | B=4 | B=1 | B=4 | B=1 | B=4 | B=1 | B=4 | Switch | NLLB-MoE | Switch | NLLB-MoE | Encoder | Decoder
GPU+Offload | 0.26111 | 0.25467 | 0.097122 | 0.066178 | 0.9224 | 0.75836 | 0.51813 | 0.35912
MoNDE | 0.72997 | 0.6093 | 0.55045 | 0.41206 | 0.85535 | 0.84802 | 0.76445 | 0.82566
MoNDE+Load-balancing | 0.89788 | 0.68042 | 0.57291 | 0.49668 | 0.88113 | 0.87554 | 0.81444 | 0.80753
Ideal GPU (∞ memory) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Notes: MoNDE achieves on average, 4.9× and 1.5× speedups for the encoder and decoder over the existing parameter offloading technique.
//
For the encoder which activates dozens of experts for each batch, MoNDE offers large improvements by avoiding large expert movement overheads.
//
The decoder operation activates only k experts for each batch.
//
MoNDE marginally underperforms the baseline offloading scheme for the smaller Switch Transformers and batch size 1.
In this case, the expert fetching overhead for the expert offloading scheme turned out to be smaller than the slowdown incurred by MoNDE’s activation movement and near-data processing, because the size of the expert transfer is small.
//
For the larger batch size and the larger NLLB-MoE model, MoNDE shows increasing improvements over the offloading technique.
This is because of three factors : more expert transfers are required for larger batch sizes, the NLLB-MoE has larger expert size, and the NLLB-MoE requires top-2 gating, meaning that 2 expert activations are required for processing a single token.
//
Our results indicate that MoNDE is more effective for larger MoE models, larger batch sizes, and larger top-k gating.

## Slide 17: Conclusion
MoNDE enables large-scale MoE inference
  Utilizes near-data processing on emerging CXL memory devices
  Replaces movement of massive experts with relatively cheap activations
  Leverages the GPU and NDP collaboration for efficient inference
  Resource-efficient solution over multi-GPU settings
Notes: This slide concludes our work.
//
MoNDE enables large-scale MoE inference by utilizing near-data processing on emerging CXL memory devices.
It replaces movement of massive experts with relatively cheap activations and leverages the GPU and NDP collaboration for efficient inference.
Furthermore, MoNDE is a resource-efficient solution, since a single MoNDE device could replace multiple GPUs in terms of memory capacity and still provide low inference latency.

## Slide 18: Thank you!
For more information and discussions
  Contact : taehyunzzz@snu.ac.kr
  More details available in paper
    Cost analysis of parameter and activation movement
    MoNDE device architecture and programming model
    Evaluations on model sensitivity and CPU
Notes: For more information on our work, please refer to our paper or reach out to the authors for discussions.
Thank you!

## Slide 19: GPU-MoNDE Communication
P2P protocols enables direct CXL-to-GPU communication (e.g., GPUDirect)
MoNDE Device
GPU
CXL I/F
PCIe Bus (BW↓)
Host CPU
CPU Intervention
①
System
Memory
②
MoNDE Device
GPU
System
Memory
CXL I/F
PCIe Bus (BW↓)
Host CPU
P2P Communication
①
2 memory copies
required

## Slide 20: Modifying the Load-balance Formula
For increased computational demands, offload more experts to the GPU
Add a scaling factor that considers the total number of tokens to process

## Slide 21: Formulation of GPU and MoNDE Workflow
  (Memory-bound → Read expert parameters from memory)
  (Compute-bound → Compute expert operations)
a
a
GPU
+ MoNDE
g
e
e
e
e
e
GPU
PCIe
MoNDE
GPU
+ Parameter
Movement
g
p
p
p
p
p
e
e
e
e
e
GPU
PCIe
Mem. Dev.
g
Gating
e
Expert
PMove
p
a
AMove
Time
Streams